## Slide 1: Final year Capstone Project– 3st Review
Real-Time Object Detection in Autonomous Vehicles Using YOLOv5
Under the supervision of
Mrs. Pallabi Kakati Assistant Professor Department of Electronics and Communication Engineering November, 2024
01. Manu kiran S |  | ID No.: 20211ECE0284
02. Nishanth T G |  | ID No : 20211ECE0265
03. Sushmitha M V |  | ID No : 20211ECE0272
Submitted to the Presidency University, Bengaluru in partial fulfillment of the requirements for the Degree of BACHELOR OF TECHNOLOGY in Electronics and Communication ENGINEERING
By

## Slide 2: Content
1.Objectives
2.Proposed Method
3.Architecture Diagram
4.Modules
5.Hardware and Software Details
6.Algorithm Details
7. Source Code Details
8.Implementation details
9.References
10.Acknowledgement

## Slide 3: Objectives
.
1 Implement YOLOv5 Framework: Integrate the YOLOv5 model into the autonomous vehicle’s perception system for real-time object detection
2 Dataset Selection and Preparation: Curate and preprocess a comprehensive dataset that includes diverse objects commonly encountered in driving scenarios (e.g., pedestrians, vehicles, traffic signs).
3 Model Training and Optimization: Train the YOLOv5 model with the prepared dataset, optimizing hyperparameters to enhance detection accuracy and speed.
4 Robustness Testing: Evaluate the model's robustness against various environmental conditions, including different lighting, weather, and urban scenarios.
5 Safety and Reliability Assessment: Analyze the impact of the object detection system on overall vehicle safety and reliability, including its influence on navigation and obstacle avoidance.

## Slide 4: Proposed Method
1 Dataset Acquisition and Preparation
Diverse Dataset: Collect a comprehensive dataset that includes a wide range of objects encountered in urban and rural environments, such as pedestrians, cyclists, vehicles, traffic signs, and road barriers.
Data Augmentation: Apply techniques like flipping, rotation, scaling, and color jittering to enhance the dataset and improve the model's generalization capabilities.
2 Model Training
YOLOv5 Configuration: Utilize YOLOv5's pre-trained weights for transfer learning, allowing the model to adapt quickly to the specific dataset.
3 Real-Time Inference Optimization
Model Pruning: Reduce the model size by pruning less significant weights, maintaining speed without sacrificing accuracy.
Quantization: Apply quantization techniques to reduce the computational load and memory footprint, allowing for faster inference on edge devices.

## Slide 5: Proposed Method
4 Sensor Integration
Multi-Sensor Fusion: Integrate data from cameras, LIDAR, and radar to enhance detection capabilities and improve overall situational awareness.
5 Implementation and Deploy
Edge Computing: Deploy the optimized YOLOv5 model on edge devices (e.g. Raspberry pi, GPUs, FPGAs) within the vehicle to facilitate low-latency processing.
6 Performance Evaluation.
Robustness Testing: Test the model's performance under different environmental conditions (lighting, weather, and traffic density) to ensure reliability.

## Slide 6: Architecture Diagram

## Slide 7: Architecture Diagram

## Slide 8
Hardware , Software , Modules Details
Hardware:
Raspberry Pi 5
Raspberry Pi camera v1.3
7 inch display
Software:
Raspberry Pi OS (System: 64-bit,version: 12 (bookworm))
Thonny IDE (version: 3.1.1)
Modules:
Pillow 10.4.0 (Python Imaging Library)
Ultralytics(YOLO-You Only Look Once) Yolov8s
Opencv-python 4.10.0.84 (CV2)
Numpy 2.1.1
picamera2

## Slide 9: Algorithm Details
Convolutional Neural Networks (CNNs) is to automatically find important
features in images (like edges, textures, and shapes)
CNN use principles from linear algebra, particularly convolution operations,
to extract features and identify patterns within images.

## Slide 10: Source Code Details
1. YOLO Model for Object Detection:
• Loads a pretrained YOLOv8 model (yolov8n.pt) for object detection on
each frame of a video named Driving.mp4.
• Extracts bounding boxes for detected objects and stores vehicle-related
ones for further processing.
2. Lane Detection:
• Applies grayscale conversion, Gaussian blur, and Canny edge detection
on each frame.
• Defines a region of interest (ROI) to focus lane detection in the road
area.
• Uses the Hough Line Transform to detect and draw lane lines on the
frame.

## Slide 11: Source Code Details
3. Distance Calculation Between Vehicles:
• Calculates the Euclidean distance between the bounding box centers of
detected vehicles.
• Converts pixel distances to real-world units, providing an estimated
distance in meters for the closest vehicle.
4. Result Display and Output:
• Annotates the frame with lane markings and displays the calculated
distance to the closest vehicle in front, if available.
• Writes the processed frames to an output video file (results.mp4) and
displays them in real-time until the user presses 'q' to exit.

## Slide 12
from PIL import Image
from ultralytics import YOLO
import cv2
import numpy as np
from picamera2 import Picamera2, Preview
# Load a pretrained YOLOv8n model
model = YOLO('yolov8s.pt')
# Initialize the PiCamera2 and configure settings
picam2 = Picamera2()
config = picam2.create_still_configuration(main={"size": (640, 480)}) # Set resolution to 640x480
picam2.configure(config)
picam2.start()
# Define the codec and create VideoWriter object to save output (optional)
fourcc = cv2.VideoWriter_fourcc(*'mp4v')
output_path = 'results.mp4'
fps = 30 # Set FPS (you can adjust this based on performance)
out = cv2.VideoWriter(output_path, fourcc, fps, (640, 480))

## Slide 13
Raspberry pi Code

## Slide 19: Implementation details
1.YOLO Model Initialization
•The code loads a pre-trained YOLOv8 model using ultralytics library
(model = YOLO('yolov8s.pt’)).
• This model is used for detecting objects in video frames.
2. Video Processing Setup
• The input video file (Driving.mp4) is read using OpenCV's VideoCapture.
• Properties like frame rate (fps), width, and height are retrieved to process
and save the output video correctly.
3. Lane Detection Function (lane_detection)
• Converts the frame to grayscale and applies Gaussian blur to reduce noise.
• Uses Canny edge detection to identify edges in the frame.
• A region of interest (ROI) is defined using a polygon mask to focus on
potential lane areas.
• Hough Line Transform is applied to detect straight lines representing lane
markings.
• Detected lines are drawn on the frame in green.

## Slide 20: Implementation details
4. Distance Calculation Function (calculate_distance)
• Computes the center points of detected bounding boxes.
• Calculates the Euclidean distance between two bounding boxes.
• A scaling factor (real_world_distance = distance / 30.0) is used to
estimate the real-world distance in meters.
5. Object Detection and Distance Estimation
• For each frame, the YOLO model runs inference to detect objects,
particularly focusing on vehicles.
• Vehicle bounding boxes are collected, and the distance between the
closest front vehicle and others is calculated.
• If a front vehicle is detected, the distance is displayed on the frame.

## Slide 21: Implementation details
6. Lane Detection and Frame Display
• Lane detection is applied to the frame, and the processed frame is saved
to an output video file (results.mp4).
• The video with overlaid lane markings and distance information is
displayed in a window.
• The loop runs until the video ends or the 'q' key is pressed
Dependencies
• cv2 (OpenCV):For video processing, image operations, and displaying
output.
• ultralytics (YOLO): For object detection using YOLOv8 model.
• numpy: For numerical operations, especially distance calculation.

## Slide 22: References
[1] A. Ihssian, K. Ismail, Modelling pedestrian safety at urban intersections using user perception, Accident Analysis & Prevention, 180, 106912, (2023) [CrossRef] [Google Scholar]
[2] X. Wang, C. Ye, M. Quddus, A. Morris, Pedestrian safety in an automated driving environment: Calibrating and evaluating the responsibility-sensitive safety model, Accident Analysis & Prevention, 192, 107265, (2023) [CrossRef] [Google Scholar]
[3] F. W. Siebert, M. Møller, A. Moe Moe Lwin, D. Albers, Illusion of safety? Safety-related perceptions of pedestrians and car drivers around 3D crosswalks, Transportation Research Part F: Traffic Psychology and Behaviour, 91, Pages 213-222, (2022) [CrossRef] [Google Scholar]
[4] Z. Meng, S. Zhao, H. Chen, M. Hu, Y. Tang and Y. Song, The Vehicle Testing Based on Digital Twins Theory for Autonomous Vehicles, in IEEE Journal of Radio Frequency Identification, 6, pp. 710-714, (2022) [CrossRef] [Google Scholar]
[5] X. Cai and X. Ding, A comparative study of machine vision-based rail foreign object intrusion detection models, 2023 IEEE 3rd International Conference on Power, Electronics and Computer Applications (ICPECA), pp. 1304-1308, Shenyang, China (2023) [Google Scholar]

## Slide 23
Acknowledgement
We would like to express our sincere thanks to the supervisor, Mrs. Pallabi Kakati, Assistant Professor, Department of Electronics and Communication Engineering for his morale boosting, meticulous guidance, co-operation and supervision throughout this project work.
We would like to owe our heartiest gratitude to Mrs. Pallabi Kakati

## Slide 24
Thank You !!!